## Slide 1
AS Computer Science · Unit 1 · Topic 1
Lesson 04
Standards, Protocols, Handshaking & the Internet
How networks actually communicate · Why networks need agreed rules · The protocols that run the internet · Establishing a connection · The internet as world-wide infrastructure
Spec 1.7.1 · 1.7.2 · 1.7.3 · 1.7.4 · 1.8.1
Notes: Fourth Unit 1 lesson. Opens by finishing off 1.7.1 from Lesson 03 — devices, addressing, transmission media and networked vs standalone — before moving into why standards matter, the named protocols, handshaking, and the internet as infrastructure. Protocols still get the most room of the four 'new' sub-topics — it's the single biggest chunk of content in this strand, which is why it also gets a Gimkit review before the formal quiz.

## Slide 2
Today · 112 min
Where we're going
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
0–5
Starter
Review Lesson 03
5–13
Video
3 key takeaways
13–24
Teach
Network devices & addressing
24–35
Teach
Media & networked vs standalone
35–39
Check
Quiz 1.7.1 ext.
39–46
Teach
1.7.2 Standards
46–51
Check
Quiz 1.7.2
51–67
Teach
1.7.3 Protocols
67–75
Gimkit
Protocol review
75–80
Check
Quiz 1.7.3
80–86
Teach
1.7.4 Handshaking
86–94
Task
Handshake builder
94–98
Check
Quiz 1.7.4
98–104
Teach
1.8.1 The internet
104–108
Check
Quiz 1.8.1
108–112
Exit ticket
3 questions + homework
By the end of today you can…
Describe networks and how they communicate — devices, addressing, transmission media, and networked vs standalone
Explain the importance of networking standards
Describe the importance and use of contemporary protocols: HTTP, FTP, SMTP, TCP/IP, IMAP, DHCP, UDP and wireless protocols
Explain the role of handshaking, and describe the internet as a world-wide communications infrastructure
Notes: The lesson now opens by finishing 1.7.1 from Lesson 03 (13–35) before standards and protocols. Protocols (51–80) still take the longest single block — teach, then a trimmed Gimkit round for fun recall, then the formal Forms quiz. Handshaking keeps its interactive task since it's the sub-topic most likely to get lost without hands-on practice; both Gimkit and the handshake task were trimmed by two minutes each to make room for the new content.

## Slide 3
Starter · 5 min
Last lesson, quick-fire
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
↺
Retrieval
Whole-class quick-fire through homework quizzes 1.5.1, 1.6.1 and 1.7.1
Answers on whiteboards, boards up together
Note which questions the class got wrong — revisit if they resurface today
?
Why start here
1.7.1 (network types) is what today builds straight on top of — devices, addressing and media all extend it before standards and protocols
Storage and fragmentation are self-contained — short recap, not a dependency
Keeps momentum before the heaviest content block of the unit so far
Notes: Quizzes from Lesson 03 were homework. 1.7.1 is the one that really matters today — everything from the network-devices content onward assumes students remember what a network is and the different types from Lesson 03.

## Slide 4
Video · 8 min
Three key takeaways
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
▶
NotebookLM summary video — embed or link here
3
While you watch
Write down 3 key takeaways
…and 1 thing you want explained
Share out at the end
Covers 1.7.1 (ext.) · 1.7.2 · 1.7.3 · 1.7.4 · 1.8.1 at summary level
Notes: Same format as Lessons 01-03. NOTE: the NotebookLM source/prompt needs updating to fold in the new 1.7.1 content (devices, addressing, media, networked vs standalone) before this lesson runs, since it now opens the lesson content rather than just standards/protocols/handshaking/internet. Park any 'want explained' items on the board — the protocol ones especially, since Gimkit and the formal quiz will address most of them.

## Slide 5
Teach · 22 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.1
Describe networks and how they communicate.
In this segment
The devices that build and manage a network
How addressing lets data reach the right device
Wired and wireless transmission, and the trade-offs of networking at all
Notes: Picks up 1.7.1 from Lesson 03, which covered network types (PAN/LAN/WLAN/WAN) and client-server vs peer-to-peer. This segment finishes the sub-topic properly: the hardware, the addressing, the media, and the pros/cons of networking itself.

## Slide 6
Teach 1.7.1
The hardware that builds a network
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.1
N
NIC
Hardware inside a device that lets it connect to a network
Every networked device needs one — wired (Ethernet) or wireless
S
Switch
Connects multiple devices within a LAN
Sends data only to the device it's addressed to, not every device
R
Router
Connects different networks together, e.g. a LAN to the internet
Directs data between networks using addresses
H
Hub
An older, simpler way to connect devices in a LAN
Broadcasts data to every device — far less efficient than a switch
W
Wireless access point
Lets wireless devices join a wired network
Turns Wi-Fi signals into a form the wired network understands
M
Modem
Connects a network to an external line, e.g. from an ISP
Converts between the network's signals and the line's signal
Notes: Six devices, deliberately grouped by role rather than alphabetically: NIC (how any device gets on a network at all), switch/hub (connecting devices within a LAN — a good contrast pair since a switch is just a smarter hub), router (between networks), access point and modem (the two 'translator' devices — wireless-to-wired, and network-to-external-line). Bridge is a fair extension mention if it comes up, but isn't a named AS requirement.

## Slide 7
Teach 1.7.1
Addressing: finding the right device
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.1
M
MAC address
A unique physical address built into a device's network hardware (its NIC)
Doesn't change — it identifies the physical device itself
Used to deliver data to the right device within a local network
I
IP address
A logical address assigned to a device on a network
Can change — assigned automatically (DHCP) or set manually
Used to route data between networks, including across the internet
Both are needed: the IP address gets data to the right network, the MAC address gets it to the right device on that network.
Notes: Nice link back to DHCP, which comes up again formally under 1.7.3 protocols later this lesson — worth flagging the connection now so it isn't a surprise. Physical vs logical is the key distinction to land.

## Slide 8
Teach 1.7.1
Transmission media: wired and wireless
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.1
Medium | Examples | Advantage | Disadvantage
Copper / twisted pair | Ethernet cables, telephone wiring | Cheap and simple to install | Limited distance and bandwidth, prone to interference
Fibre optic | High-speed backbone and broadband links | Very high bandwidth, long distance, resistant to interference | More expensive to buy and install
Wireless (radio) | Wi-Fi, Bluetooth, cellular | No cables needed — devices can move freely | Usually slower and less secure than wired, prone to interference
Notes: Keep this at comparison level, not deep technical detail — the useful takeaway is the speed/cost/mobility trade-off, which directly sets up the networked-vs-standalone advantages and disadvantages on the next slide.

## Slide 9
Teach 1.7.1
Networked vs standalone
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.1
+
Advantages of networking
Share resources — printers, files, internet connections
Centralised management — updates, backups and security controlled from one place
Easy communication between devices and users
–
Disadvantages of networking
A bigger security risk — more points where an attacker could get in
If the network goes down, every connected device can be affected
Costs more to set up and maintain than standalone computers
Notes: Closes out the extended 1.7.1 content by zooming back out from the technical detail (devices, addressing, media) to the bigger-picture question: why network computers together at all, and what's the cost of doing so. Good bridge into standards next — one of networking's costs is complexity, which is exactly what standards exist to manage.

## Slide 10
Check · 4 min
Quiz 1.7.1 (extended) — how networks communicate
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.1
Describe networks and how they communicate
Quiz link — Microsoft Forms: [ADD LINK / QR HERE]
Notes: Run the extended 1.7.1 quiz via Microsoft Forms — devices, addressing, transmission media, networked vs standalone.

## Slide 11
Teach · 7 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.2
Explain the importance of networking standards.
In this segment
What a networking standard actually is
Why the industry agreed on them
What would go wrong without them
Notes: Short and conceptual — the goal is a clear 'why', not a long list. This sets up why protocols (next segment) exist at all: protocols ARE the standards.

## Slide 12
Teach 1.7.2
Why networking standards matter
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.2
1
Interoperability
Hardware and software from different vendors can work together
Without shared standards, building networks that easily share information would be difficult or impossible
2
No vendor lock-in
Customers aren't forced to buy every device from one company
Standards mean genuine choice between suppliers
3
Competition & price
Open standards promote competition between vendors
More competition helps hold prices down
4
Easier development
Software and hardware can be developed one layer at a time
Developers build to the standard, not to every possible device
Notes: All four points come straight from the WJEC mark scheme's indicative content. A quick check question: 'what would the internet look like if every manufacturer used their own private rules?' — nudges towards interoperability as the headline reason.

## Slide 13
Check · 5 min
Quiz 1.7.2 — networking standards
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.2
Explain the importance of networking standards
Quiz link — Microsoft Forms: [ADD LINK / QR HERE]
Notes: Run the 1.7.2 quiz via Microsoft Forms.

## Slide 14
Teach · 16 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.3
Describe the importance and the use of a range of contemporary protocols, including HTTP, FTP, SMTP, TCP/IP, IMAP, DHCP, UDP and wireless communication protocols.
In this segment
What each named protocol actually does
Why each one matters — not just what it stands for
Wired protocols first, then wireless
Notes: The biggest single content block in Topic 1 so far — eight named protocols. Keep pace brisk on the table slide; depth comes from the 'importance' column, not from dwelling on each row individually.

## Slide 15
Teach 1.7.3
Protocols that run the internet
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.3
Protocol | What it does | Why it matters
HTTP | Transfers web pages between a server and a browser | Lets any browser request and display pages the way the author intended
FTP | Transfers files between computers over a network | Built-in error checking and re-transmission if something goes wrong
SMTP | Sends email from a client to a server, or server to server | A standard way of passing email between different mail servers
IMAP | Retrieves and syncs email, keeping messages on the server | Same inbox on every device, without using up local storage
TCP/IP | The core protocol suite the internet runs on — breaks data into packets and routes them | The basic, shared language every device on the internet uses
DHCP | Automatically assigns IP addresses to devices joining a network | Frees addresses no longer in use back to the pool for reallocation
UDP | Sends data fast, with very little error-recovery | Suits video/audio streaming, where speed matters more than the odd lost packet
Notes: This table is deliberately the reference students will use for Gimkit and the quiz — the 'why it matters' column is what separates an AS-level answer from just naming the protocol, which the mark scheme explicitly rewards.

## Slide 16
Teach 1.7.3
Wireless communication protocols
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.3
📶
Wi-Fi (802.11)
Wireless local area networking
Connects devices to a router within a building or site
Used for most home and office wireless internet access
◉
Bluetooth
Short-range, low-power connections
Device-to-device — headphones, keyboards, wearables
A wireless PAN, not a full network
📡
Cellular (4G / 5G)
Wide-area mobile data over the phone network
Internet access without a fixed Wi-Fi connection
5G adds higher speed and lower latency than 4G
Notes: Keep this light — the spec asks for contemporary wireless protocols, not deep technical detail. The useful distinction is scale: Bluetooth (PAN) vs Wi-Fi (LAN) vs cellular (WAN), echoing the network-types slide from Lesson 03.

## Slide 17
Gimkit · 8 min
Protocol review — game time
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
Launch Gimkit here
(game code / link)
🎮
Before you launch
Questions cover all 7 named protocols plus wireless
Recall only — the formal quiz right after this checks understanding
Table from the last two slides stays up as a reference if needed
Notes: Fast-paced recall to cement the protocol names before the formal check. Keep the reference table visible for students who want it — this is about retrieval practice, not a closed-book test.

## Slide 18
Check · 5 min
Quiz 1.7.3 — protocols (formal)
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.3
Describe the importance and use of contemporary protocols
Quiz link — Microsoft Forms: [ADD LINK / QR HERE]
Notes: Run the 1.7.3 quiz via Microsoft Forms. Should move quickly given the table, Gimkit and reference material already covered.

## Slide 19
Teach · 6 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.4
Explain the role of handshaking.
In this segment
What handshaking actually means
Why devices need to do it before sending data
The simple three-step shape it usually takes
Notes: Short teach, then straight into the interactive task — handshaking is easy to state but easy to forget, so hands-on practice does more work here than a long explanation.

## Slide 20
Teach 1.7.4
Handshaking: agreeing to talk before talking
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.4
?
What it is
When a computer system establishes a device's readiness to communicate
Happens before any real data is sent
!
Why it matters
Confirms both devices are ready and agree on how to communicate
Avoids data being sent to a device that isn't listening, or can't understand it
1
Request
Device A signals it wants to communicate
2
Acknowledge
Device B responds — I'm ready, here's how I can communicate
3
Confirm
Device A confirms — agreed, data transfer begins
Notes: The phone-call analogy lands well: 'hello, can you hear me?' → 'yes, go ahead' → conversation starts. This same three-step shape is what the interactive task walks students through with a proper request/acknowledge/confirm exchange.

## Slide 21
Interactive task · 8 min
Handshake Sequence Builder
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
Put the steps of a device handshake into the correct order, and see why the order itself matters.
How it works
A shuffled set of handshake steps. Reorder them, check, and get feedback on exactly where the sequence breaks if it's wrong.
Why order matters
If a device sends data before the handshake completes, the receiving device may not be ready — data gets lost or misread. Order is the whole point.
Notes: Individually or in pairs. Link/QR code goes here once built. This is the only dedicated interactive task this lesson — Gimkit already covers protocol recall, so this one is reserved for the sub-topic that most needs hands-on reinforcement.

## Slide 22
Check · 4 min
Quiz 1.7.4 — handshaking
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.7.4
Explain the role of handshaking
Quiz link — Microsoft Forms: [ADD LINK / QR HERE]
Notes: Run the 1.7.4 quiz via Microsoft Forms. Should be quick after the task.

## Slide 23
Teach · 6 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.8.1
Describe the internet in terms of a world-wide communications infrastructure.
In this segment
Zooming out from single networks to the internet itself
"A network of networks"
How today's four sub-topics all fit underneath this one idea
Notes: The natural closing idea for the whole networking strand — standards, protocols and handshaking are all things that make the internet, as a network of networks, actually work.

## Slide 24
Teach 1.8.1
A network of networks
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.8.1
THE INTERNET
LAN
school
LAN
office
LAN
home
LAN
college
LAN
business
Each LAN is its own network. The internet connects them all together — a world-wide infrastructure built from smaller networks, not one single network.
Notes: Deliberately simple diagram — the point is scale and composition, not technical routing detail. Tie back explicitly: standards (1.7.2) let these different networks interoperate, protocols (1.7.3) are the rules they use to talk, and handshaking (1.7.4) is how any two devices on this diagram start a conversation.

## Slide 25
Check · 4 min
Quiz 1.8.1 — the internet
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1.8.1
Describe the internet as a world-wide communications infrastructure
Quiz link — Microsoft Forms: [ADD LINK / QR HERE]
Notes: Run the 1.8.1 quiz via Microsoft Forms.

## Slide 26
Exit ticket · 4 min
On your whiteboard
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
1
Give one reason networking standards matter.
2
Name a protocol used for sending email, and one used for web pages.
3
Explain in one sentence why handshaking happens before data is sent.
Notes: Q1 checks 1.7.2, Q2 checks 1.7.3, Q3 checks 1.7.4. Model answers: (1) e.g. lets hardware/software from different vendors interoperate; (2) SMTP for email, HTTP for web pages; (3) so both devices confirm they're ready and agree how to communicate before any real data is sent.

## Slide 27
Homework · for next lesson
Before Lesson 05
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 04
★
Extension (optional)
Pick one protocol from today and find a real example of it failing or being exploited (e.g. an FTP or DHCP security issue)
One paragraph on what went wrong and why the protocol's rules matter
↺
If anything felt shaky
Reread the protocols table and the handshaking section of the Topic 1 notes
Redo any Handshake Sequence Builder attempt you got wrong first time
All four of today's quizzes were completed in lesson — nothing new to do there
Notes: Homework is deliberately light — today's four quizzes were all completed in lesson, so this is consolidation/extension only, not new content. This also closes out the 1.7/1.8 networking strand before moving on to the next topic.