## Slide 1
AS COMPUTER SCIENCE · UNIT 1 · TOPIC 2
Logical Operations
Lesson 1: Truth Tables & Notation
From AND, OR, NOT & XOR to building your own truth tables from scratch

## Slide 2
LESSON OBJECTIVES
By the end of this lesson, you will be able to…
1
Use correct Boolean notation
and apply the order of operations: brackets → NOT → AND → OR
2
Draw truth tables for AND, OR, NOT and XOR
using a systematic method, always working from 00 through to 11
3
Build truth tables with three or more inputs
using the 2^n rule to work out how many rows you need
4
Read a completed truth table
and write the simplest Boolean expression it represents
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
2

## Slide 3
STARTER
Two switches, one bulb
This circuit only has ONE path from the battery to the bulb — the current has to pass through both switches.
A
B
bulb
Discuss: for every combination of switch A and switch B being ON or OFF, does the bulb light up?
Switch A | Switch B | Bulb?
OFF | OFF | ?
OFF | ON | ?
ON | OFF | ?
ON | ON | ?
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
3

## Slide 4
STARTER — DEBRIEF
Series and parallel → AND and OR
SERIES CIRCUIT
Both switches must be ON for current to flow
AND
A . B — true only when A = 1 AND B = 1
A | B | A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
PARALLEL CIRCUIT
Either switch being ON is enough for current to flow
OR
A + B — true when A = 1 OR B = 1 (or both)
A | B | A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
4

## Slide 5
DIRECT TEACH
Boolean notation you need to know
Symbol | Operator | Meaning
A . B (or AB) | AND | True only when both A and B are true
A + B | OR | True when at least one of A or B is true
Ā (or ¬A) | NOT | Reverses the value of A
A ⊕ B | XOR | True when A and B are different
ORDER OF OPERATIONS
Brackets → NOT → AND → OR
Just like BIDMAS: AND behaves like ×, OR behaves like +
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
5

## Slide 6
DIRECT TEACH
Good practice: always start at 00, end at 11
Before filling in any values, list every combination of inputs in order — this way you never miss a row or repeat one. It's the same pattern as counting in binary: 00, 01, 10, 11.
A | B
0 | 0
0 | 1
1 | 0
1 | 1
← start here
← end here
Why this matters later
Once you're building tables with 3 inputs and no columns given, this habit is what stops you from missing a row on an exam question — it becomes 000, 001, 010, 011, 100, 101, 110, 111.
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
6

## Slide 7
GUIDED TASK
AND
Build the truth table for A AND B
Work through each row systematically (00 → 11). Ask yourself: are BOTH inputs 1?
Write your table on your whiteboard/worksheet before checking.
A | B | A.B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
7

## Slide 8
GUIDED TASK
OR
Build the truth table for A OR B
Same systematic order. Ask yourself: is AT LEAST ONE input 1?
A | B | A+B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
8

## Slide 9
GUIDED TASK
NOT
Build the truth table for NOT A
NOT only takes ONE input, so you only need 2 rows, not 4.
What does NOT do to each value?
A | Ā (NOT A)
0 | 
1 | 
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
9

## Slide 10
GUIDED TASK
XOR
Build the truth table for A XOR B
XOR means “exclusive or.” Ask yourself: are A and B DIFFERENT from each other?
A | B | A⊕B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
10

## Slide 11
CHECK YOUR WORK
Answers: the four core operators
AND
A | B | A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
OR
A | B | A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
NOT
A | Ā
0 | 1
1 | 0
XOR
A | B | A⊕B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Keep this slide handy — you'll use these four tables constantly for the rest of the topic.
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
11

## Slide 12
?
Quiz time
Complete the truth table multiple choice quiz before we move on — AND, OR, NOT and XOR.
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
12

## Slide 13
DIRECT TEACH
Scaling up: how many rows do you need?
The number of rows in a truth table depends on how many inputs there are.
Inputs (n) | Rows (2^n)
1 | 2
2 | 4
3 | 8
4 | 16
3 INPUTS → 8 ROWS
Extend the same 00→11 habit to three variables — count in binary from 000 to 111:
A | B | C
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
13

## Slide 14
GUIDED TASK
SCAFFOLDED
Complete this 3-input table
Work left to right, one column at a time. Use the operator tables from earlier if you need reminding.
A . B
then (A . B) + C
A | B | C | A.B | (A.B)+C
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
14

## Slide 15
INDEPENDENT TASK
UNAIDED
Now build these completely from scratch
No columns are given this time. Decide your own working order using the precedence rules, and remember: 8 rows, starting at 000.
1
X = A ⊕ B + C.(A + B)
based on a genuine WJEC/Eduqas exam question
2
Y = (A + C) . (B ⊕ C)
3
Z = Ā . (B + C)
stretch: try it without writing out Ā as a separate column first
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
15

## Slide 16
DIRECT TEACH
The reverse skill: table → expression
Sometimes you're given a completed truth table and asked for the simplest Boolean expression. Use the “Find the 1s” method:
1
Find the 1s
Look only at the rows where the output is 1 — ignore every row where it's 0
2
Write a term per row
For each of those rows, AND the inputs together — use the letter if it's 1, NOT the letter if it's 0
3
OR the terms together
Combine all your terms with OR — that's your expression
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
16

## Slide 17
WORKED EXAMPLE
Applying “Find the 1s”
A | B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Output = 1 on two rows:
Row: A = 0, B = 1 → Ā . B
Row: A = 1, B = 0 → A . B̄
OR the two terms together:
Ā.B + A.
(This is the same pattern as XOR — worth noticing!)
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
17

## Slide 18
INDEPENDENT PRACTICE
Your turn: find the expression
Table 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Table 2
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
Table 3
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
For each table: find the 1s, write a term per row, OR them together. One of these should simplify to something you already recognise — which operator is it?
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
18

## Slide 19
PLENARY
What have we covered today?
✓
Boolean notation and order of operations
✓
Truth tables for AND, OR, NOT and XOR
✓
The 2^n rule for scaling up to more inputs
✓
Building 3-input tables completely from scratch
✓
“Find the 1s” — reading a table back into an expression
Next lesson: masking, clearing registers, and the Boolean identity laws.
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
19

## Slide 20
TEAMS POST
Lesson summary & key vocabulary
TODAY'S OBJECTIVES
• Boolean notation & order of operations
• Truth tables for AND, OR, NOT, XOR
• Scaling up with the 2^n rule
• Finding an expression from a completed table
HOMEWORK
Finish the independent practice tasks if not completed in class.
KEY VOCABULARY (EN / CY)
Truth table
[verify – Y Termiadur Addysg]
Logical operator
[verify – Y Termiadur Addysg]
Boolean expression
[verify – Y Termiadur Addysg]
AND / OR / NOT / XOR
[verify – Y Termiadur Addysg]
Welsh terms are placeholders — confirm against Y Termiadur Addysg before posting.
Topic 2 – Logical Operations | Lesson 1: Truth Tables & Notation
20