## Slide 1
AS Computer Science · Unit 1 · Topic 1
Lesson 03
Storage, Fragmentation & Networks
Secondary storage devices · Fragmentation & defragmentation · How networks communicate
Spec 1.5.1 · 1.6.1 · 1.7.1
Notes: Third Unit 1 lesson. We left off at 1.4.2 last time. Today: 1.5.1 secondary storage, 1.6.1 fragmentation (builds directly off the HDD content from 1.5.1), and a lighter pass over 1.7.1 network basics — protocols/standards/handshaking are a later lesson, not today.

## Slide 2
Today · 90 min
Where we're going
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
0–5
Starter
Review Lesson 02
5–15
Video
3 key takeaways
15–27
Teach
1.5.1 Secondary storage
27–40
Interactive
Pick the Right Storage
40–45
Check
Quiz 1.5.1
45–55
Teach
1.6.1 Fragmentation
55–66
Interactive
Defrag visualiser
66–71
Check
Quiz 1.6.1
71–81
Teach
1.7.1 Networks
81–86
Check
Quiz 1.7.1
86–90
Exit ticket
3 questions + homework
By the end of today you can…
Compare the functional characteristics of contemporary secondary storage devices
Explain fragmentation and its consequences, and describe why defragmentation is needed
Describe networks and how they communicate
Notes: Storage and fragmentation share a teach block naturally — HDD characteristics from 1.5.1 feed straight into why fragmentation matters in 1.6.1. Networks is deliberately lighter: 1.7.1 is just network types and how they communicate — protocols, standards and handshaking are separate spec points for a future lesson.

## Slide 3
Starter · 5 min
Last lesson, quick-fire
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
↺
Retrieval
Whole-class quick-fire through homework quizzes 1.3.1, 1.4.1 and 1.4.2
Answers on whiteboards, boards up together
Note which questions the class got wrong — revisit if they resurface today
?
Why start here
Today's storage and networking content is new — no direct dependency on the fetch-execute cycle
But keeping registers and I/O ticking over protects earlier learning
Short and quick, so most of the lesson is new content
Notes: Quizzes from Lesson 02 were homework. Kept brief today — unlike Lessons 01→02, today's content doesn't build directly on the retrieval, so 5 minutes is enough.

## Slide 4
Video · 10 min
Three key takeaways
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
▶
NotebookLM summary video — embed or link here
3
While you watch
Write down 3 key takeaways
…and 1 thing you want explained
Share out at the end
Covers 1.5.1 · 1.6.1 · 1.7.1 at summary level
Notes: Same format as Lessons 01 and 02. Park any 'want explained' items on the board — the storage/fragmentation ones especially, since the interactive tasks later will answer most of them.

## Slide 5
Teach · 12 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.5.1
Compare the functional characteristics of contemporary secondary storage devices.
In this segment
Six contemporary storage devices, side by side
The characteristics that make one device better suited than another
Speed of access, cost per unit, portability, capacity, durability
Notes: Frame this as revisiting the memory hierarchy from Lesson 01 — secondary storage is 'below' RAM, non-volatile, and the choice between devices always comes down to trading off the same handful of characteristics.

## Slide 6
Teach 1.5.1
Six contemporary storage devices
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.5.1
HDD
Magnetic platters, moving read/write head. Cheap per byte, large capacity, slower than SSD.
SSD
No moving parts, flash memory. Fast access, more expensive per byte than HDD.
Optical (CD/DVD/Blu-ray)
Laser-read discs. Cheap, portable, limited capacity, easily damaged.
Magnetic tape
Serial access, very cheap per byte. Slow, but reliable for large-scale archival backup.
Flash / USB drive
Small, portable solid-state storage. Fast, convenient, limited capacity.
Cloud storage
Data stored on remote servers over a network. Accessible anywhere, depends on network speed.
Notes: Fast tour — one sentence of character per device. The comparison table on the next slide is where the detail (and the exam-style language) lives.

## Slide 7
Teach 1.5.1
Comparing them on the same characteristics
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.5.1
Device | Speed of access | Cost per unit | Portability | Typical capacity
HDD | Fast (but slower than SSD) | Low | Low–medium | Large (TBs)
SSD | Very fast | Higher | Medium | Medium–large
Optical disc | Slow | Very low | High | Small (GBs)
Magnetic tape | Slow (serial access) | Very low | High | Very large (archival)
Flash / USB | Fast | Low–medium | Very high | Small–medium
Cloud storage | Depends on network | Ongoing (subscription) | Accessible anywhere | Scalable / very large
A 'compare' answer always trades characteristics against each other — e.g. tape is cheap and huge but far too slow for daily access; SSD is fast but costs more per byte.
Notes: This table is the reference for the interactive task that follows — every scenario in 'Pick the Right Storage' is really asking students to weigh these same five columns against each other.

## Slide 8
Interactive task · 13 min
Pick the Right Storage
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
Read a real-world scenario. Choose the best-fit storage device, and justify it against the characteristics you've just learned.
Example scenario
“A large company needs to keep 10 years of financial records, rarely accessed but must never be lost.”
How it works
Several scenarios, each with 4 device options. Pick one, then choose the characteristic that justifies it best. Feedback explains why the top choice wins.
Notes: Individually or in pairs. Link/QR code goes here once built. Circulate and listen for justification language — 'because it's cheaper per byte' or 'because access needs to be fast' is the exam-style phrasing we want to hear.

## Slide 9
Check · 5 min
Quiz 1.5.1 — quick-fire
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.5.1
Secondary storage characteristics
Topic 01 › Quizzes › 1.5.1
Notes: Run the 1.5.1 quiz. Should move quickly after the comparison table and the interactive task.

## Slide 10
Teach · 10 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.6.1
Explain fragmentation and its consequences, and describe the need for defragmentation.
In this segment
Why HDD files end up scattered across the disk
How fragmentation slows down access
What defragmentation does — and why SSDs are different
Notes: Builds directly on the HDD content just taught — the physical moving parts that make HDDs slower than SSD are exactly what makes fragmentation a performance problem in the first place.

## Slide 11
Teach 1.6.1
How data gets fragmented on a HDD
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.6.1
platter + read/write head
1
The physical picture
Data is stored on a spinning magnetic platter, in tracks and sectors
A read/write head moves across the disk to reach each sector
2
Where fragmentation comes from
A file doesn't always fit in one contiguous space
It gets split and stored in whatever free sectors are available — often scattered across the disk
The more the disk fills and empties over time, the more fragmented it becomes
Notes: The diagram is deliberately simple — platter, spindle, arm, head. The key idea for the mark scheme: fragmentation means a file's data is split and stored on different parts of the disk, and HDD's magnetic technology (a physically moving head) is what makes that costly.

## Slide 12
Teach 1.6.1
Consequences, and what defragmentation does
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.6.1
!
Consequences of fragmentation
The read/write head must move to several different positions to read one file
Each move takes time — slower access speeds overall
More fragmentation → more head movement → more wear
✓
What defragmentation does
Physically rearranges fragmented data so each file's parts sit closer together
Fewer positions for the head to move between
Access speeds improve as a result
?
Common exam mix-up: SSDs don't need defragmenting
SSDs have no moving head — random access to any location costs the same, so scattered data isn't slower to read
SSDs use a different maintenance process (TRIM) instead — worth a sentence, not required depth for this spec point
Notes: The SSD/TRIM card is flagged because it's a very common source of confused exam answers — students sometimes describe 'defragmenting an SSD'. Keep the TRIM detail brief; it's context, not required spec content.

## Slide 13
Interactive task · 11 min
Disk fragmentation visualiser
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
A simplified disk map with a file scattered across it. Defragment it and watch what changes.
A1
B1
A2
A3
B2
A4
Before — scattered
A1
A2
A3
A4
B1
B2
After — defragmented
▶
How it works
Drag or tap to move blocks — the task tracks how many head movements each file needs
Defragment and compare the movement count before vs after
A short question set checks the 'why' behind what you just watched happen
Notes: Individually or in pairs. Link/QR code goes here once built. The visual before/after mirrors this slide's diagram — point that continuity out if students seem unsure what they're looking at.

## Slide 14
Check · 5 min
Quiz 1.6.1 — quick-fire
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.6.1
Fragmentation and defragmentation
Topic 01 › Quizzes › 1.6.1
Notes: Run the 1.6.1 quiz. If short on time, this is fine to run at a brisk pace given the visualiser just covered the mechanics directly.

## Slide 15
Teach · 10 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.7.1
Describe networks and how they communicate.
In this segment
The main types of network, from personal to worldwide
Client-server vs peer-to-peer communication
Wired vs wireless transmission, at a basic level
Notes: Deliberately kept narrow — just network types and the basic idea of how devices communicate over them. Protocols, networking standards and handshaking are separate spec points, saved for a later lesson.

## Slide 16
Teach 1.7.1
From personal to worldwide
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.7.1
PAN
Personal Area Network
A single person's own devices — e.g. phone to smartwatch or wireless earbuds
Typical range
Metres
LAN
Local Area Network
One site — e.g. a school or office building
Typical range
One building / site
WLAN
Wireless LAN
A LAN using wireless connections instead of cables
Typical range
One building / site
WAN
Wide Area Network
Connects LANs across a large area — the Internet is the largest WAN
Typical range
Cities / countries / global
Notes: Scale is the organising idea — PAN smallest, WAN largest, and the Internet is explicitly named as the largest WAN (sets up the later 'internet as world-wide infrastructure' spec point without teaching it yet).

## Slide 17
Teach 1.7.1
How devices on a network communicate
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.7.1
Client-server
Server
Client 1
Client 2
Client 3
Clients request; a central server provides the resource or service — e.g. a website, a file share.
Peer-to-peer
Peer 1
Peer 2
Peer 3
Peer 4
Every device can act as both client and server — sharing directly with each other, with no central server.
Notes: Keep this brief — the key distinction is 'central server vs no central server'. Wired vs wireless as a second dimension can be a quick verbal add-on rather than its own diagram: cable vs radio waves, both can carry either model.

## Slide 18
Check · 5 min
Quiz 1.7.1 — quick-fire
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1.7.1
Networks and how they communicate
Topic 01 › Quizzes › 1.7.1
Notes: Run the 1.7.1 quiz. Keep pace brisk — this segment was intentionally light on content.

## Slide 19
Exit ticket · 4 min
On your whiteboard
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
1
Name a storage device and one situation where it would be the wrong choice.
2
Explain why fragmentation slows down a HDD but not an SSD.
3
Give one difference between a LAN and a WAN.
Notes: Q1 checks 1.5.1, Q2 checks 1.6.1, Q3 checks 1.7.1. Model answers: (1) e.g. magnetic tape for a portable field data collector — too slow; (2) HDD has a moving read/write head that must travel between scattered sectors, SSD has no moving parts so any location costs the same to access; (3) e.g. a LAN covers one site, a WAN connects LANs across a large area / the Internet is a WAN.

## Slide 20
Homework · for next lesson
Before Lesson 04
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 03
★
Extension (optional)
Research one contemporary cloud storage provider and note its stated durability/reliability claims
Compare against the characteristics table from today
↺
If anything felt shaky
Reread the storage and fragmentation sections of the Topic 1 notes
Redo any 'Pick the Right Storage' scenario you got wrong first time
All three of today's quizzes were completed in lesson — nothing new to do there
Notes: Homework is deliberately light — today's three quizzes were all completed in lesson, so this is consolidation/extension only, not new content.