## Slide 1
CPU
AS Computer Science · Unit 1 · Topic 1
Lesson 01
Inside the Box
Hardware & communication elements · Computer architecture & Von Neumann · Memory & caching
Spec 1.1.1 · 1.2.1 · 1.2.2
Notes: Welcome. First proper teaching lesson of Unit 1. Today's three spec points: 1.1.1 hardware and communication elements and how they connect; 1.2.1 computer architecture including Von Neumann; 1.2.2 types of memory and caching. Whiteboards and pens out before we start.

## Slide 2
Today · 90 min
Where we're going
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
0–5
Starter
Label the open case
5–13
Video
3 key takeaways
13–30
Teach
1.1.1 Hardware & connections
30–40
Check
Quiz 1.1.1
40–56
Teach
1.2.1 Architecture & Von Neumann
56–70
Collab task
Where does it live?
70–82
Teach
1.2.2 Memory & caching
82–90
Exit ticket
3 questions + homework
By the end of today you can…
Name the key hardware and communication elements of a PC and say what each connects through
Describe the CU, ALU, the five registers and the three buses — and state what makes an architecture Von Neumann
Place registers, cache, RAM, virtual memory, ROM, SSD and HDD in a memory hierarchy and explain what caching is for
Notes: Run through the roadmap quickly. Copper boxes are things students DO; grey boxes are teacher-led. Point out that the collaborative task comes before the memory teach on purpose: they will have a go first, then we fix what went wrong.

## Slide 3
Starter · 5 min
What can you see?
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
?
In pairs, on whiteboards
Label every component you can name
For each one: what does it plug into?
Bonus: which parts are memory?
Prior knowledge check — no wrong answers yet
Notes: 5 minutes max. Listen for the misconceptions we will target later: 'cache is RAM', 'clock speed = performance', 'ROM is old storage'. Do not correct yet — note them on the board for later. Photo to be sourced (see lesson note).

## Slide 4
Video · 8 min
Three key takeaways
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
▶
NotebookLM summary video — embed or link here
3
While you watch
Write down 3 key takeaways
…and 1 thing you want explained
Share out at the end
Covers 1.1.1 · 1.2.1 · 1.2.2 at summary level
Notes: Play the NotebookLM video (to be generated from the Topic 1 notes). Collect a few takeaways and 'want explained' items — park the latter on the board and tick them off as the lesson covers them. Check register names in the video match the spec: PC, MAR, MDR, CIR, ACC.

## Slide 5
Teach · 17 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.1.1
Identify and describe the hardware and communication elements of contemporary computer systems and how they are connected.
In this segment
The motherboard as the hub
Each component: what it does, and what it connects through
Communication elements: buses, controllers, interfaces, NIC
Notes: Frame the segment with one question we will ask of every component: 'what does it connect THROUGH?' That is the 'how they are connected' half of the spec statement and the bit students miss.

## Slide 6
Teach 1.1.1
The motherboard is the hub
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.1.1
MOTHERBOARD
system bus · chipset · slots · ports
CPU
socket
RAM
DIMM slots
Storage (SSD / HDD)
SATA · NVMe
GPU
PCIe
Sound card / NIC
PCIe (or on-board)
Input / output devices
USB · HDMI · Bluetooth
PSU
power connectors
Everything connects to the motherboard — directly (socket, slot) or through a port — and talks over buses and interfaces.
Notes: Build this map live on the board if you prefer — this slide is the finished version. Ask for each block: what is it for, and what does it connect through? The orange line is the interface — that is the exam-relevant vocabulary (PCIe, SATA, NVMe, USB, HDMI, Bluetooth).

## Slide 7
Teach 1.1.1
The core: processing, memory, storage
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.1.1
C
CPU
Executes instructions — the 'brain'
Control Unit (CU) directs operations
Arithmetic Logic Unit (ALU) does maths & logic
Registers: tiny, fastest storage inside the CPU
Cache: high-speed memory for frequent data
Connects: CPU socket → system bus to RAM
M
Memory
RAM — volatile working memory for running programs
ROM — non-volatile; holds BIOS/UEFI firmware
Cache — on/near the CPU, cuts latency
Connects: DIMM slots → memory bus
S
Storage
HDD — magnetic platters, high capacity, mechanical
SSD — flash memory, no moving parts, faster
Non-volatile: keeps data with the power off
Connects: SATA or NVMe (PCIe) interface
Notes: Keep 'cache' brief here — it comes back properly in 1.2.2. The connection line at the bottom of each card is the 'how they are connected' part of the spec. Quick check: which of these three is volatile? (RAM only.)

## Slide 8
Teach 1.1.1
Around the core: I/O, graphics, sound, power
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.1.1
I/O
Input & output
Input: keyboard, mouse, scanner, mic
Output: monitor, printer, speakers
Connect: USB, HDMI, DisplayPort, Bluetooth
G
GPU
Dedicated processor for images, video, 3D
Own memory (VRAM)
Connects: PCIe slot
♪
Sound card
DSP processes audio
DAC: digital → analogue (out)
ADC: analogue → digital (in)
Integrated on-board, or PCIe / USB
P
PSU
Converts mains AC to the DC the parts need
Powers motherboard, drives, GPU via cables
No data — power only
Notes: Sound card gets more space in the notes than students expect — DAC/ADC is a nice link to data representation later (Topic 4). Ask: why does a microphone need an ADC but speakers need a DAC?

## Slide 9
Teach 1.1.1
Communication elements
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.1.1
CPU
RAM
I/O devices
Data bus
Address bus
Control bus
The system bus
System bus
Data bus carries the data · Address bus says where · Control bus carries commands (read, write, interrupt)
Controllers & interfaces
I/O controllers (USB, SATA) manage traffic between CPU and devices; USB, Thunderbolt, Bluetooth connect peripherals
Network interface (NIC)
Wired (Ethernet) or wireless (Wi-Fi) — PCIe or on-board. Talks to routers/switches using TCP/IP
Notes: Introduce the three buses by name here — we come back to direction (uni/bidirectional) in 1.2.1. NIC and protocols are only a mention today; they are the back half of Topic 1 (1.7–1.8).

## Slide 10
Teach 1.1.1
Connection map — copy this down
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.1.1
Component | Job | Connects through
CPU | Executes instructions (CU, ALU, registers, cache) | CPU socket → system bus
RAM | Volatile working memory | DIMM slots → memory bus
ROM | Firmware (BIOS/UEFI) for booting | On the motherboard
SSD / HDD | Non-volatile long-term storage | SATA · NVMe (PCIe)
GPU | Renders graphics | PCIe
Sound card | DSP, DAC, ADC for audio | On-board · PCIe · USB
NIC / Wi-Fi | Joins the network | PCIe · on-board
Input / output | Keyboard, mouse, monitor, printer… | USB · HDMI · DisplayPort · Bluetooth
PSU | Converts and supplies power | Power cables (no data)
Notes: This is the reference table for the exam. 'Identify and describe … and how they are connected' = column 1 + column 2 + column 3. Give a minute to copy or photograph it.

## Slide 11
Check · 10 min
Quiz 1.1.1 — quick-fire
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.1.1
15 multiple-choice questions
Question on screen → write the letter on your whiteboard
Boards up on 3
One-line justification from a volunteer
Tally your score — we revisit the weak ones next lesson
Quiz file
1.1.1 – Identify and describe the hardware and communication elements…docx
Topic 01 › Quizzes
Watch for: Q3 (RAM vs cache), Q7 (PCIe), Q10 (data bus)
Notes: Open the 1.1.1 quiz document and run through it question by question. If time is tight, do Q1–10 and set 11–15 with homework. Note class weak spots on the board.

## Slide 12
Teach · 16 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.1
Identify and describe the main components of contemporary computer architecture, including Von Neumann architectures.
In this segment
Inside the CPU: Control Unit, ALU, registers, cache
The five registers — what each one holds
The three buses and their direction
Von Neumann: shared memory, sequential, stored program — and the bottleneck
Notes: We zoom in from the whole box to the CPU. Architecture = the design and organisation of the hardware and how the parts interact.

## Slide 13
Teach 1.2.1
Inside the CPU
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.1
CPU
Control Unit (CU)
directs & coordinates
ALU
arithmetic & logic
Registers
PC · MAR · MDR
CIR · ACC
Cache
L1 · L2 · L3
frequently used data
Four parts to name
CU — fetches, decodes, coordinates; tells everything else what to do
ALU — add, subtract, compare, AND/OR/NOT
Registers — tiny, fastest storage; each has one job
Cache — keeps frequently used data close to the cores
Notes: Students often think the ALU 'runs the program'. It doesn't — the CU does the running, the ALU does the sums. Registers HOLD things; CU and ALU DO things. That distinction is a misconception we listed.

## Slide 14
Teach 1.2.1
The five registers — what each one holds
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.1
PC
Program Counter
Address of the NEXT instruction to fetch. Increments after each fetch (unless a jump).
MAR
Memory Address Register
The address in memory being read from or written to. Sent out on the address bus.
MDR
Memory Data Register
The data just read from, or about to be written to, memory. Buffer between CPU and RAM.
CIR
Current Instruction Register
The instruction being executed right now, split into opcode and operand for decoding.
ACC
Accumulator
Intermediate results from the ALU.
Mnemonic to try: PC → MAR → MDR → CIR → ACC is the order they appear in a fetch. Full walk-through in the fetch-execute lesson (week 7).
Notes: One line each. Do NOT walk the whole fetch-execute cycle today — that is lesson 4 (week 7). The aim now is that students can name the five and say what each HOLDS. Quick check: which register holds an address? (Two: PC and MAR.) Which holds data? (MDR, ACC.) Which holds an instruction? (CIR.)

## Slide 15
Teach 1.2.1
Three buses — what travels, and which way
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.1
CPU
Memory
& I/O
Data bus
carries the data itself
both ways
Address bus
carries where in memory (from MAR)
CPU → memory only
Control bus
carries read · write · interrupt · clock
both ways
Exam favourite: the address bus is unidirectional — memory never tells the CPU an address.
Notes: Link back to slide 9 — same three buses, now with direction. Ask: why can't the address bus be bidirectional? (Only the CPU decides which location to access.) Width of the data bus = how much data per transfer; width of the address bus = how many locations can be addressed — a nice stretch point.

## Slide 16
Teach 1.2.1
Von Neumann architecture (1945)
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.1
Input
CPU
Control Unit
ALU
Registers
MEMORY
instructions
+ data
Output
system bus
Four defining features
ONE memory for instructions AND data
Sequential — one instruction at a time, in order
A Control Unit drives fetch & execute
Stored program — change the program, not the hardware
Instructions and data share the same memory and the same bus.
Notes: The single most important idea: instructions and data live together in one memory, reached over one bus. Everything else (the bottleneck, Harvard) follows from that. 'Stored program' is why a computer can be reprogrammed — contrast with a fixed-function calculator.

## Slide 17
Teach 1.2.1
Why it won — and where it hurts
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.1
+
Advantages
Simple to design and build
Flexible — update the program, keep the hardware
Cost-effective: one memory, one bus
!
The Von Neumann bottleneck
Instructions AND data must squeeze through the same bus
CPU is faster than memory — it waits
Memory bandwidth becomes the limit
→
Working around it
Harvard architecture — separate instruction and data memory (embedded systems)
Cache hierarchies — L1/L2/L3 (next segment)
Multi-core, pipelining, out-of-order execution (next lesson)
Notes: Bottleneck = a 'describe/explain' exam question. The answer needs both halves: shared bus AND CPU-memory speed gap. Harvard is the contrast — quiz 1.2.1 Q13 asks it. Pipelining/multi-core are previews only; they belong to 1.2.3 next lesson.

## Slide 18
Collab task · 14 min
Where does it live?
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
Sort these nine into the pyramid by speed and size, then tag each volatile or non-volatile.
Registers
L1 cache
L2 cache
L3 cache
RAM
Virtual memory
ROM
SSD
HDD
fast · small
slow · large
Groups of 3 · one screen · interactive HTML task
Enter your group name · Check when done · Answers revealed in the debrief, not before
Notes: Open the 'Where does it live?' HTML task (to be built) on group devices. Circulate: listen for reasoning about ROM and virtual memory — those are the deliberately awkward ones. Do NOT reveal answers yet; compare group pyramids on the board and use the disagreements to drive the 1.2.2 teach.

## Slide 19
Teach · 12 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.2
Describe different types of memory and caching.
In this segment
Debrief the pyramids → the memory hierarchy
Types of memory: RAM, ROM, cache, virtual, flash, registers, secondary
Caching: CPU cache (L1/L2/L3) and disk cache
Notes: Start from what the groups produced. Put two contrasting pyramids side by side and ask the class to argue it out before showing the answer.

## Slide 20
Teach 1.2.2
The memory hierarchy
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.2
Registers
inside the CPU · CPU speed · bytes
L1 · L2 · L3 cache
on the CPU · KB–MB · SRAM
RAM
main memory · GB · DRAM · volatile
Virtual memory
disk pretending to be RAM · slow
SSD · HDD · flash
secondary storage · TB · non-volatile
↑ faster · smaller · costlier per byte
↓ slower · larger · cheaper per byte
ROM sits outside the ladder: non-volatile firmware on the motherboard, read at boot.
Notes: Reveal tier by tier against the groups' answers. The two argument-starters: virtual memory is on disk but is used like RAM (so sits between them functionally), and ROM is not really on the speed ladder at all — its job is firmware. Volatile: registers, cache, RAM. Non-volatile: ROM, flash, SSD, HDD.

## Slide 21
Teach 1.2.2
Types of memory — the ones the exam names
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.2
RAM
Volatile; fast; holds running programs and data
DRAM (main memory) · SRAM (cache)
ROM
Non-volatile; written at manufacture / firmware update
BIOS/UEFI — used to boot
Cache
Small, very fast, next to the cores
L1 smallest/fastest → L3 largest, shared
Virtual memory
Part of the disk used as an extension of RAM when it's full
Lets more/bigger programs run — slowly
Flash
Non-volatile solid-state — USB sticks, SSDs, cards
Faster than HDD; no power needed to keep data
Registers & secondary
Registers: CPU-speed, tiny, inside the processor
Secondary (HDD/SSD): non-volatile, large, slow
Notes: Two describers the mark scheme wants for each type: volatility and typical use. Push on 'virtual memory is disk, not RAM' and 'ROM is firmware, not old storage'.

## Slide 22
Teach 1.2.2
Caching: keep what you need next, closer
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.2.2
CPU asks
L1?
L2?
L3?
RAM
Disk
hit → stop here. miss → drop down a level and try again. Each step down is slower.
CPU cache
Holds frequently used instructions and data
L1 per core · L2 per core/shared · L3 shared by all cores
Reduces the time waiting on RAM
Disk cache
RAM (or a buffer on the drive) holding frequently read blocks
Speeds up reads/writes to HDD or SSD
Analogy
Desk (registers) → drawer (cache) → filing cabinet (RAM) → archive (disk)
You don't fetch from the archive if it's in your drawer
Same rule for hits and misses
Notes: The hit/miss flow is the concept behind 'describe caching'. Ask: why not make everything L1? (Cost, physical size, heat.) Tie to the bottleneck from 1.2.1: cache exists because RAM can't keep up with the CPU.

## Slide 23
Teach 1.2.2
Four things people get wrong
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1.1.1 · 1.2.1 · 1.2.2
✕
Cache is a type of RAM
Cache is SRAM on/next to the CPU. RAM is main memory (DRAM) on the motherboard.
✕
Faster clock = faster computer
Cache size, cores, bus width and memory speed all matter — the bottleneck is usually memory.
✕
ROM is old storage
ROM is non-volatile firmware (BIOS/UEFI) used to boot — not somewhere you save files.
✕
Virtual memory is extra RAM
It's disk space used as if it were RAM. It works, but it's slow.
Notes: Go back to the misconceptions you parked from the starter and tick them off here.

## Slide 24
Exit ticket · 8 min
On your whiteboard
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
1
Name one component and the interface it connects to the motherboard through.
2
What is the Von Neumann bottleneck?
3
Why is L1 cache smaller than L3?
Notes: Q1 checks 1.1.1, Q2 checks 1.2.1, Q3 checks 1.2.2. Model answers: (1) e.g. GPU → PCIe, SSD → SATA/NVMe; (2) shared bus for instructions and data plus CPU faster than memory, so the CPU waits; (3) faster memory is more expensive and physically larger per byte, and L1 must sit inside the core.

## Slide 25
Homework · for next lesson
Before Lesson 02
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 01
R
Read
Topic 1 notes — section 1.2.2 Types of memory and caching
Make a one-page summary: each memory type, volatile or not, what it's used for
Q
Complete
Quiz 1.2.1 — Fundamentals of computer architecture (15 MCQ)
Quiz 1.2.2 — Types of memory and caching (15 MCQ)
We go through both as the starter next lesson, then move on to parallel processing (1.2.3)
Notes: Both quizzes live in Topic 01 › Quizzes. Next lesson opens with a 15-minute retrieval block: 1.1.1 again (spaced), then review of 1.2.1 and 1.2.2. Quiz 1.2.1 Q13–15 (Harvard, pipelining, multi-core) lead straight into 1.2.3.