## Slide 1
AS Computer Science · Unit 1 · Topic 1
Lesson 02
Many Hands, One Cycle
Llawer o Ddwylo, Un Gylchred
Parallel processing · The fetch-execute cycle · Input & output devices
Spec 1.2.3 · 1.3.1 · 1.4.1 · 1.4.2
Notes: Second Unit 1 lesson. We left off at 1.2.2 last time. Today: 1.2.3 parallel processing, 1.3.1 the fetch-execute cycle (the big one — registers finally do something), and a light pass over 1.4.1/1.4.2 input and output. Welsh terms appear as a small violet caption strip on section slides and under a few key diagram labels — bilingual reinforcement, not the main content; check compound terms against the WJEC Welsh-medium glossary before teaching through the medium of Welsh.

## Slide 2
Today · 90 min
Where we're going
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
0–8
Starter
Review 1.2.1 / 1.2.2
8–15
Video
3 key takeaways
15–35
Teach + Check
1.2.3 Parallel processing
35–47
Teach
1.3.1 Fetch-execute core
47–65
Interactive task
Register tracker
65–76
Debrief + Check
1.3.1 sticking points
76–88
Teach + Check
1.4.1 / 1.4.2 I/O
88–90
Exit ticket
3 questions + homework
By the end of today you can…
Describe and explain parallel processing — task division, concurrency, coordination, scalability
Describe the fetch-execute cycle, showing how data moves from RAM into PC, MAR, MDR, CIR and ACC
Describe contemporary input/output methods and devices, and explain what makes each suitable for a situation
Notes: The fetch-execute block (35–76) is the longest because it's the highest-value spec point in Topic 1. 1.4 is deliberately compressed — straightforward content, consolidated through the quizzes rather than a long teach.

## Slide 3
Starter · 8 min
Last lesson, quick-fire
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
↺
Retrieval
Whole-class quick-fire through homework quizzes 1.2.1 and 1.2.2
Answers on whiteboards, boards up together
Note which questions the class got wrong — revisit if they resurface today
?
Why start here
1.2.1 (architecture, registers) feeds directly into today's fetch-execute cycle
1.2.2 (memory) is what the cycle reads from and writes to
Spacing this retrieval improves what sticks from Lesson 01
Notes: Quizzes 1.2.1 and 1.2.2 were homework after Lesson 01. This is the payoff — both feed straight into today, especially the five registers, which are about to do real work for the first time.

## Slide 4
Video · 7 min
Three key takeaways
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
▶
NotebookLM summary video — embed or link here
3
While you watch
Write down 3 key takeaways
…and 1 thing you want explained
Share out at the end
Covers 1.2.3 · 1.3.1 · 1.4.1 · 1.4.2 at summary level
Notes: Same format as Lesson 01. Park any 'want explained' items on the board — the fetch-execute ones especially, since the interactive task later will answer most of them.

## Slide 5
Teach · 12 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.2.3
Prosesu Cyfochrog
Describe and explain parallel processing.
In this segment
Sequential vs parallel execution
Task division, concurrency, coordination, scalability
Advantages vs challenges, and where it's used
GEIRFA ALLWEDDOL · KEY VOCABULARY
Parallel processing
Prosesu cyfochrog
Core / multi-core
Craidd / amlgraidd
Synchronisation
Cydamseru
Notes: Frame with the Von Neumann bottleneck from Lesson 01: parallel processing is one of the ways round it. Welsh terms in the panel are for reinforcement — introduce them briefly, don't dwell.

## Slide 6
Teach 1.2.3
One queue, or many at once?
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.2.3
Sequential
Task 1
Task 2
Task 3
Task 4
One core. Tasks queue and run one after another — total time is the sum of every task.
Parallel
Core 1
Core 2
Core 3
Core 4
Task 1
Task 2
Task 3
Task 4
Several cores. Tasks are divided and run at the same time — total time shrinks towards the length of the longest single task.
The catch: dividing the work, coordinating the cores and combining results all cost time too — parallel isn't free.
Notes: Visual contrast: one lane vs several lanes. Ask: if 4 tasks take 2 minutes each, how long sequentially (8 min) vs on 4 cores (about 2 min, plus overhead)? That overhead is the bridge into the next slide's challenges.

## Slide 7
Teach 1.2.3
Four ideas behind parallel processing
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.2.3
1
Task division
Break a big job into smaller independent pieces that can run separately
2
Concurrency
Multiple pieces genuinely running at the same time, on separate cores
3
Coordination
Cores must communicate and stay in step so results combine correctly
4
Scalability
Add more cores, handle more work — up to a point
Notes: These four are the building blocks the 'describe and explain' exam answer is built from. Quick check: which of the four is the one most likely to go wrong? (Coordination — race conditions, waiting on each other.)

## Slide 8
Teach 1.2.3
Why bother — and where it bites
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.2.3
+
Advantages
Increased speed
Efficiency — more done per second
Scalability
Handles large data sets
!
Challenges
Task dependency — some steps must wait for others
Synchronisation overhead
Resource contention
Added complexity
→
Where it's used
Supercomputers
Graphics processing (GPUs)
Search engines
Machine learning
Notes: Pair with an advantage against a challenge: speed vs synchronisation overhead is the classic 'explain' pairing in mark schemes.

## Slide 9
Check · 8 min
Quiz 1.2.3 — quick-fire
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.2.3
Describe and explain parallel processing
Question on screen → answer on whiteboard
Boards up on 3
One volunteer justifies their answer
Tally the score — carry weak points into the debrief
Topic 01 › Quizzes › 1.2.3
Notes: Run the 1.2.3 quiz. If short on time, this is the one to trim first — the fetch-execute block that follows is the priority.

## Slide 10
Teach · 12 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.3.1
Cylchred Cyrchu-Gweithredu
Describe the fetch-execute cycle, showing how data can be read from RAM into registers.
In this segment
The five registers, now in motion
Fetch → Decode → Execute, stage by stage
How an address in RAM becomes data in a register
GEIRFA ALLWEDDOL · KEY VOCABULARY
Fetch / Decode / Execute
Cyrchu / Datgodio / Gweithredu
Register
Cofrestr
Instruction
Cyfarwyddyd
Notes: This is the centrepiece of the lesson. Lesson 01 introduced the five registers as things that 'hold' values — today they finally do something. Keep this teach segment tight (12 min); the interactive task is where the depth happens.

## Slide 11
Teach 1.3.1
The five registers — quick recap
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.3.1
PC
Program Counter
Cyfrif Rhaglen
Address of the next instruction
MAR
Memory Address Register
Cofrestr Cyfeiriad Cof
The address currently being accessed
MDR
Memory Data Register
Cofrestr Data Cof
Data just read from, or about to be written to, memory
CIR
Current Instruction Register
Cofrestr Cyfarwyddyd Cyfredol
The instruction being decoded / executed
ACC
Accumulator
Cronnwr
Intermediate results from the ALU
Notes: From Lesson 01 — this time every register is about to do real work in the cycle on the next slide. Welsh names shown small under the English; don't read them all out, they're for the display.

## Slide 12
Teach 1.3.1
The fetch-execute cycle
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.3.1
1
PC → MAR
PC
Address of the next instruction is copied into MAR
2
MAR → RAM
MAR
MAR sends that address out on the address bus
3
RAM → MDR
MDR
The instruction stored there is copied into MDR
4
MDR → CIR
CIR
The instruction moves into CIR to be decoded
5
Decode
CU
The Control Unit splits CIR into opcode + operand
6
Execute
ALU / ACC
ALU runs the operation; result goes to ACC. PC increments, ready for the next fetch.
Fetch (1–4) · Decode (5) · Execute (6) — then the cycle repeats from the new PC.
Cyrchu (1–4) · Datgodio (5) · Gweithredu (6)
Notes: This is the reference diagram — the interactive task walks the same six stages one at a time with a question gating each. Point out MAR (address) vs MDR (data) explicitly here; that's the confusion the debrief slide expects to resurface.

## Slide 13
Teach 1.3.1
Watch it happen — Little Man Computer
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.3.1
LMC simulator — live demo
(link / screenshot here)
▶
Load a short program
e.g. add two numbers and output the result
Step one instruction at a time
Narrate each register change against the diagram on the last slide
Notes: Keep this to about 5 minutes — the point is to see the six stages happen in a real (simplified) machine before students work through it themselves in the interactive task. Have a short add-two-numbers program ready to load rather than writing it live.

## Slide 14
Interactive task · 18 min
Fetch-execute register tracker
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
Step through one instruction cycle. Answer the question at each stage before you can continue.
PC → MAR
MAR → RAM
RAM → MDR
MDR → CIR
Decode
Execute
Each stage
A question gates progress — “which register just changed?”, “what does MAR hold right now?”. Immediate feedback explains a wrong answer before you continue.
At the end
A completion summary shows which stages needed a retry — that's what drives the debrief that follows.
Notes: Individually or in pairs, one device per pair. Link/QR code goes here once built. Circulate and watch for the same two sticking points named on the debrief slide: MAR vs MDR, and exactly when PC increments.

## Slide 15
Debrief · 5 min
Where did the cycle catch people out?
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.3.1
!
MAR vs MDR
MAR holds an ADDRESS — where to look
MDR holds the DATA — what was found there
Easy mix-up: both are 4-letter registers that look similar on the diagram
?
When does PC increment?
After the instruction is fetched — not after it's executed
So PC is already pointing at the NEXT instruction while the current one is still being decoded/executed
Notes: Pull these from the task's completion summaries if you can see them, or just ask the class which questions tripped them up. These two are the classic sticking points regardless.

## Slide 16
Check · 6 min
Quiz 1.3.1 — quick-fire
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.3.1
The fetch-execute cycle
Topic 01 › Quizzes › 1.3.1
After the tracker and the debrief this should move quickly — treat it as confirmation, not first exposure.
Notes: Should be quick given the task and debrief just happened. If the class flew through it, bank the extra minutes for the I/O section.

## Slide 17
Teach · 6 min
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.4.1 · 1.4.2
Dulliau Mewnbwn ac Allbwn
Describe the use of contemporary methods and devices for input and output — and explain their suitability in different situations.
In this segment
A quick tour of I/O methods and devices
What makes each one the right (or wrong) choice
GEIRFA ALLWEDDOL · KEY VOCABULARY
Input device
Dyfais fewnbwn
Output device
Dyfais allbwn
Suitable / appropriate
Addas
Notes: Deliberately short — this is the lightest content in Topic 1. Combine 'describe' and 'explain suitability' into one pass rather than teaching them separately.

## Slide 18
Teach 1.4.1 · 1.4.2
Device, and where it's the right choice
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.4.1 · 1.4.2
Device | Type | Best suited to…
Touchscreen | Input | Kiosks, tablets — intuitive, no extra hardware, but imprecise for detailed work
Keyboard & mouse | Input | Precise text entry and navigation — desktop / office work
Barcode / QR scanner | Input | Retail and stock control — fast, low error rate on repetitive data
Microphone (voice input) | Input | Hands-free or accessibility contexts — driving, mobility impairment
Monitor | Output | General visual output — most contexts
3D / laser printer | Output | Physical documents, or prototyping and manufacture
Speakers | Output | Audio feedback, accessibility for visually impaired users
Braille display | Output | Accessibility — tactile output for blind or low-vision users
Notes: Fast pace — this is reference material more than a teach. Ask a few quick 'why not X here' questions (e.g. why not a touchscreen for a stock-take? too slow/imprecise vs a scanner) to hit the 'explain suitability' half of the spec without dwelling.

## Slide 19
Check · 6 min
Quizzes 1.4.1 and 1.4.2
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1.4.1 · 1.4.2
Two short quizzes, back to back
Topic 01 › Quizzes › 1.4.1, 1.4.2
Notes: Both quizzes are short — run them together rather than as two separate blocks.

## Slide 20
Exit ticket · 2 min
On your whiteboard
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
1
Name one advantage AND one challenge of parallel processing.
2
Put PC, MAR, MDR, CIR, ACC in fetch-execute order and say what each holds.
3
Name a device and one situation where it would be the wrong choice.
Notes: Q1 checks 1.2.3, Q2 checks 1.3.1, Q3 checks 1.4.1/1.4.2. Model answers: (1) e.g. speed up vs synchronisation overhead; (2) PC (next address) → MAR (address to access) → MDR (data found) → CIR (instruction to decode) → ACC (result); (3) e.g. touchscreen for detailed spreadsheet entry.

## Slide 21
Homework · for next lesson
Da iawn — before Lesson 03
AS Unit 1 · Topic 1 Hardware & Communication · Lesson 02
★
Extension (optional)
A second LMC program to run at home
Log the register values each cycle in a trace table — same format as the Topic 9 trace tables
↺
If anything felt shaky
Reread the fetch-execute section of the Topic 1 notes
Redo any tracker question you got wrong first time
All four of today's quizzes were completed in lesson — nothing new to do there
Notes: Homework is deliberately light — today's four quizzes were all completed in lesson, so this is consolidation/extension only, not new content. 'Da iawn' = 'well done'.