## Slide 1: How data travels
Topic 3: Data transmission | Lesson 1 of 3
Serial and parallel | Simplex, half duplex and full duplex
1
1
1
1
1
1
1
1
Notes: Welcome. Lesson 1 of 3 on Topic 3 (spec 3.1.1 and 3.1.2). Post the Teams message with objectives and key terms before the lesson starts.

## Slide 2: Lesson objectives
Describe serial and parallel transmission
Spec 3.1.1
Explain the advantages and disadvantages of each, including skew and crosstalk
Spec 3.1.1
Describe simplex, half duplex and full duplex transmission
Spec 3.1.2
Apply each method to a real example, as the exam expects
Spec 3.1.2
Notes: Objectives 1 and 2 cover 3.1.1 (first half of the lesson), 3 and 4 cover 3.1.2. Point out that the topic has appeared on every Unit 1 paper since 2022.

## Slide 3: Key terms | Termau allweddol
English | Cymraeg
Serial transmission | Trawsyrru cyfresol
Parallel transmission | Trawsyrru paralel
Skew | Sgiw
Crosstalk | Croes-siarad
Simplex | Simplecs
Half duplex | Hanner duplecs
Full duplex | Dublecs llawn
Notes: DRAFT Welsh terminology: verify every term against Y Termiadur Addysg before posting to Teams. Skew and crosstalk in particular need checking.

## Slide 4: Starter: which way does it travel?
10 min on your own
Sort each example into one of the three groups.
TV broadcast
Walkie-talkie
Phone call
Keyboard to PC
Baby monitor
Video call
One way only
Both ways, taking turns
Both ways at once
Notes: No terminology yet: students sort on intuition (as with the light-switch starter in Topic 2). Answers: one way = TV broadcast, keyboard to PC, baby monitor. Taking turns = walkie-talkie. At once = phone call, video call. Keep the groups visible; slide 17 names them. Self-paced HTML version to follow.

## Slide 5: Watch: data transmission in five minutes
5 min
Insert NotebookLM video here
While you watch, note down:
one difference between serial and parallel
one reason parallel is used less today
which starter group a phone call belongs to

## Slide 6: Serial and parallel
Spec 3.1.1: describe serial and parallel transmission, their advantages and disadvantages

## Slide 7: Serial transmission
Sender
Receiver
0
0
1
0
0
0
1
0
The letter D (01000100) travelling one bit at a time down a single wire
How it works
Data is sent one bit at a time
Bits travel one after another down a single channel
Bits arrive in the same order they were sent
Where it is used
USB and Thunderbolt
Ethernet network cables
SATA drives and PCIe expansion cards
Long-distance links between devices
Notes: Definition first: one bit at a time, single channel. Stress that "single wire" is a simplification: USB has power and ground wires too, but one data path in each direction.

## Slide 8: Parallel transmission
Sender
Receiver
0
0
1
1
0
0
0
0
0
0
0
1
0
0
1
0
D
A
How it works
Several bits are sent at the same time
Each bit has its own wire (8, 16 or 32 wires)
A whole byte can arrive on one clock tick
Where it is used
Buses inside the computer, e.g. CPU to RAM
Older printer cables (IEEE 1284)
Older IDE hard drive cables
Notes: Ask: if both use the same clock speed, how much faster is parallel with 8 wires? (8 times, in theory.) Then ask why we stopped using parallel printer and IDE cables. That question leads into the next slide.

## Slide 9: Why parallel struggles over distance
Sender
Receiver
0
1
0
0
0
1
0
0
Bits drift apart. Orange bits miss the clock tick.
Skew
Signals on different wires travel at slightly different speeds. The longer the cable, the further the bits drift out of sync.
Crosstalk
Wires running side by side interfere with each other electrically, which can corrupt bits.
Result
Parallel has to run at a slower clock speed, or over short distances only. Serial has neither problem.
Notes: Key idea for the top grades: skew is WHY parallel is limited to short distances. The mark scheme also credits needing thicker wire over long distances to reduce signal degradation.

## Slide 10: Serial vs parallel
 | Serial | Parallel
Bits sent | One at a time | Several at the same time
Speed | Slower per clock tick, but can be clocked much faster | Faster over short distances
Distance | Reliable over long distances | Short distances only (skew)
Cost | Cheaper: fewer wires | More expensive: more wires
Interference | No crosstalk between data wires | Crosstalk between wires
Notes: Students copy or photograph this table. Push the speed row: older textbooks say "serial is slower", but modern serial links beat parallel because they can run at much higher clock speeds.

## Slide 11: So why is almost everything serial now?
Parallel is faster per clock tick, but skew and crosstalk stop it from being clocked faster. With one data wire, serial can be pushed to much higher clock speeds.
Printer
Then: Parallel port
Now: USB
Hard drive
Then: IDE (parallel)
Now: SATA (serial)
Expansion card
Then: PCI (parallel)
Now: PCIe (serial)
Notes: Don't answer this fully yet. Students discover it themselves in Bit race mission 3, then return to it in the plenary.

## Slide 12: Task: Bit race
15 min in pairs
1
Inside the computer, both clocks at ×1. Which cable wins, and by roughly how much?
2
Switch to the network cable. What happens to the parallel message, and why?
3
Network cable with crosstalk on. Can serial beat parallel with no errors?
Then answer the exam question at the bottom of the page together, before revealing the mark scheme.
Open the Bit race link on Teams.
Notes: Pairs, one screen. Circulate during mission 2: ask "what is the word for that?" (skew). Mission 3 reveals that serial can be clocked faster. Answers are in the tool behind reveals.

## Slide 13: Exam question: Summer 2025
Q3(a) Describe two advantages and two disadvantages of parallel transmission over serial transmission. [4]
Read the question carefully: it asks about parallel compared with serial. Two marks are available for advantages and two for disadvantages, so four advantages only scores 2.

## Slide 14: Mark scheme: 2025 Q3(a)
Advantages (max 2)
Data is transmitted at a higher speed
Works well for short-distance communication
A set of bits is transferred simultaneously
Disadvantages (max 2)
More expensive because extra wires are needed
Over long ranges the wire must be thicker to reduce signal degradation
Multiple communication channels are required
Crosstalk can occur when multiple data lines are used

## Slide 15: Check: serial and parallel quiz
5 min
Insert link to your serial and parallel quiz

## Slide 16: Simplex, half duplex and full duplex
Spec 3.1.2: describe simplex, half duplex and full duplex transmission methods

## Slide 17: Three transmission methods
Simplex
A
B
Data travels in one direction only.
Example: Keyboard to computer, TV broadcast
Half duplex
A
B
Data travels in both directions, but only one direction at a time.
Example: Walkie-talkie
Full duplex
A
B
Data travels in both directions at the same time.
Example: Phone call, broadband
Notes: Examples credited in the 2023 mark scheme: keyboard (simplex), walkie-talkie (half duplex), broadband (full duplex). For half duplex the dashed arrow means "possible, but not while A is sending".

## Slide 18: Back to the starter
One way only
Simplex
TV broadcast, keyboard to PC, baby monitor
Both ways, taking turns
Half duplex
Walkie-talkie
Both ways at once
Full duplex
Phone call, video call
Notes: Students check their starter sort and relabel the groups with the technical terms.

## Slide 19: Getting the marks
Earns the mark
"Data can travel in both directions, but only one direction at a time" (half duplex)
"Data can travel in both directions at the same time" (full duplex)
A definition plus a separate, correct example
Loses the mark
"Half duplex sends data both ways" (doesn't say one at a time)
"Full duplex is faster" (doesn't describe the method)
Reusing the same example, or an example that doesn't fit (e.g. "the internet" for simplex)

## Slide 20: Task: Duplex detective
15 min in pairs
1
Read the scenario card
2
Choose simplex, half duplex or full duplex
3
Write a one-line justification
4
Pick the explanation that would earn the mark
Watch for the tricky ones: some devices use different methods for different jobs. Agree with your partner before you submit.
Notes: Duplex detective HTML to follow. Tricky cards include a baby monitor (simplex) vs a two-way baby monitor with talk-back (half duplex), a CB radio, and a games controller with rumble.

## Slide 21: Check: transmission methods quiz
5 min
Insert link to your simplex and duplex quiz

## Slide 22: Exam practice: Summer 2023
6 min on your own
Q6 Describe simplex, half duplex and full duplex data transmission methods and give an example use for each. [6]
Simplex
Description (1)
Example (1)
Half duplex
Description (1)
Example (1)
Full duplex
Description (1)
Example (1)
Finished early? 2016 Q5(a) asks for the same three descriptions for only 3 marks, with no examples. Rewrite your answer to fit it.

## Slide 23: Mark scheme: 2023 Q6
Simplex
Data can only travel in one direction (1)
e.g. keyboard (1)
Half duplex
Data can travel in both directions, but only in one direction at any given time (1)
e.g. walkie-talkie (1)
Full duplex
Data can travel in both directions at the same time (1)
e.g. broadband (1)
For 2016 Q5(a): one mark for each description only.
Notes: Students self-mark in a different colour pen. Also accept other sensible examples (e.g. TV broadcast, CB radio, phone call). Collect a show of hands on 6/6.

## Slide 24: If parallel is faster, why is USB serial?
Answer in two sentences on the Teams post. Use the words skew and clock speed.
Notes: Model answer: Parallel sends more bits per clock tick, but skew and crosstalk mean it must run at a lower clock speed and over short distances. Serial has one data wire, so it has no skew and can be clocked much faster, which makes it faster overall and reliable over longer cables. Next lesson: multiplexing, switching and packets.